Xsaitekpanel Configuration
for
TorqueSim BN-2B Islander
Author
- Name: Andrew Gransden
- X-Plane.org ID: scotflieger
Change Log
Version 1.0
- 29 Jun 2020
- Initial Start
Prerequisites

The following X-Plane 11 Plugins are required to run the BN-2B Islander configurations:

FlyWithLua - https://forums.x-plane.org/index.php?/files/file/38445-flywithlua-ng-next-generation-edition-for-x-plane-11-win-lin-mac/

XSaitekPanels - https://forums.x-plane.org/index.php?/files/file/14646-xsaitekpanels-linwinmac3264/

The configurations file are designed to operate with the Saitek/Logitech Switch, Multi and Radio panels. No additional software is required.
Installation
- Download and unzip the archive using your favorite zip utility.
- Copy the “xsaitekpanels.ini” file to the Torquesim BN-2B Islander aircraft directory. This is the same directory that holds the BN-2B Islander.acf file (X-Plane 11\xaircraft\x-aviation\).
- Copy the “Torquesim_Islander_BN-2B_Xsaitekpanels.lua” file to the FlyWithLua scripts directory (X-Plane 11\Resources\plugins\FlyWithLua\Scripts).
Operation
Controlled by xsaitekpanels.ini file
Switch Panel Engine Start Switch
With the Islander twin engine configuration the rotary switch panel switch operates as follows:
- OFF
- All magnetos off
- External Supply off
- RIGHT
- External Supply on
- Right Magnetos 1 and 2 on
- LEFT
- External Supply on
- Left and Right Magnetos 1 and 2 on
- BOTH/ALL
- External Supply on
- Left and Right Magnetos 1 and 2 on
- Starts Left Engine
- START
- External Supply on
- Left and Right Magnetos 1 and 2 on
- Starts Right Engine
After starting return switch to LEFT position.
Switches
The following switches are functional:
- BAT - operates Main Battery switches
- ATT - operates Left and Right Engine Generators switch
- Avionics Master - operates Avionics switch
- Fuel Pump - operates Left and Right Fuel Pump switches
- De-Ice - not implemented
- Pitot Heat - operates Pitot and Stall Warn Heaters
- Cowl - operates Carb Heat levers
- Panel - operates Panel Light knob (behind yoke)
- Beacon - operates Beacon light switch
- Nav - operates Nav Lights switch
- Strobe - not implemented
- Taxi - operates Landing Left light switch
- Landing - operates Landing Right light switch
- Gear Lever - operates Parking Brake (up on/down off)
Multi Panel
All knobs and buttons operate as normal.
Note:
- The AP button does not illuminate.
- IAS is not implemented.
- Auto-Throttle switch is not implemented.
- Flap lever operates the flaps but VC switch not animated.
- Pitch Trim not fully tested.
Radio Panel
All radio knobs and buttons operate as normal.
Controlled by LUA file
The LUA file defines the DataRefs and commands required to make the panels operate. Several additional functions and related commands are defined to implement specific Islander actions on the Switch Panel:
- Left and Right Engine Start switches
- Panel light knob - not working
- Pitch Trim wheel
Commands and DataRefs
All newly created Commands and DataRefs use the identifier: awg/islander/